## Slide 1: NodeGeoSpatialServices
Node Geospatial Services for the RIF

## Slide 2: RIF NodeGeoSpatialServices
NodeGeoSpatialServices integrates a number of Node modules as web services to provide remote web services to:
Convert shapefiles to GeoJSON;
Validate, aggregate, clean and simplify converted shapefile data suitable for use in maptiles;
Convert GeoJSON to a) TopoJSON and b) Well known text;
Create hierarchy tables;
Create maptiles;
Create polygonal and population weighted centroids.

## Slide 3: RIF NodeGeoSpatialServices (2)
Replaces the Postgres only prototype that uses psql scripts, PL/pgsql and shp2psql;
Will require PostGres and PostGIS in the server for access to OGSS functionality;
Designed to be portable to SQL server;

## Slide 4: RIF NodeGeoSpatialServices (3)
The inputs to NodeGeoSpatialServices will be one , usually 3+ shapefiles;
The outputs, sets of:
Maptiles;
Portable geospatial data.

## Slide 5: RIF NodeGeoSpatialServices (4)
The NodeGeoSpatialServices client would normally store data either in flat files (e.g. maptiles) or a GeoSptial database (e.g. PostGIS);
The client is not required to carry out any additional geospatial processing;
Since multiple processing steps are envisaged the server will be required to maintain state;
It will do this by saving data as GeoJson in a file or in a PostGIS/SQL server table;
Maintaining state will reduce the data be transferred to a minimum.

## Slide 6: RIF NodeGeoSpatialServices (5)
It is not intended at present to support:
Shapefile formats not supported by Node SHP/MapShaper;
To convert a) TopoJSON or b) Well known text to GeoJSON;
To convert a) TopoJSON or b) GeoSON to shapefiles.
This is technically possible, but requires GDAL; PostGIS uses GDAL.
This is only required to assist in visualising the data and producing outputs; RIF NodeGeoSpatialServices are currently only intended for data loading.

## Slide 7: Population weighted centroids
Population weighted centroids requires population data and additional non standard processing (i.e. there is no OGSS standard function) in PostGIS.

## Slide 8: GeoNode
NodeGeoSpatialServices should not be confused with GeoNode (http://geonode.org/):
GeoNode is a platform for the management and publication of geospatial data. It brings together mature and stable open-source software projects under a consistent and easy-to-use interface allowing users, with little training, to quickly and easily share data and create interactive maps.
GeoNode is essentially Open Google Earth/Maps with an emphasis on accessibility via easy to use interfaces and good metadata.

## Slide 9: Workflow

## Slide 10: Workflow example - Upload
The Shp2GeoJSON service will:
Upload a set shapefiles, e.g. five UK2011 (census output area, lower level super output area, ward, local area district, region);
Geometry projection detection will be automatic (i.e. then ESRI projection .prj file is mandatory);
The specified shapefile geometry column will be converted to GeoJSON and stored in a file on the server as their original name;
The directory will be the session id name, one will be created for you at the first upload and must be used in all subsequent operations;
You will not get the GeoJSON data back unless you request it.

## Slide 11: simplifyGeoJSON
The simplifyGeoJSON service will load, validate, aggregate, clean and simplify converted shapefile data suitable for use in maptiles:
Run once per shapefile in the set;
Validate aggregate and clean geospatial data:
  SELECT 'LEVEL4' AS geolevel_name, level4 AS area_id,
  NULL::Text AS name,
  ST_Union(
  CASE WHEN ST_IsValid(geom) = FALSE THEN ST_MakeValid(geom)
  ELSE geom END) AS geom
  /* Make valid if required, Union polygons together */,
  ROW_NUMBER() OVER (ORDER BY level4) AS gid
  FROM x_sahsu_level4
  GROUP BY level4;
Additionally the data needs to be converted to a MultiPolgon using ST_Multi(). The rows are now unique per area so can now take a primary key.

## Slide 12: simplifyGeoJSON (2)
This service will load the previous GeoJSON file into the database will a sequentially number table name;
The session id, table name and file name will be stored in a control table;
The loaded data is stored in the native geometric datatype as the column SHAPEFILE_GEOMETRY with the shapefile projection;
Validation, aggregate and clean. The area id and area name fields must be defined. The area name will be defaulted from the area id if required, area id must not be null;
After validation, aggregation and cleaning the geospatial data will be simplified;

## Slide 13: simplifyGeoJSON (3)
The simplification will support default zoomlevels of 6, 8 and 11;
The columns will be named OPTIMISED_GEOMETRY_<zoomlevel> for database geometry data and OPTIMISED_GEOJSON_<zoomlevel> for the JSON representation;
It addition to the current Douglas-Peucker, Visvalingam simplification with the "effective area" metric and weighted Visvalingam simplification (the default) will be supported;
By default, the simplified GeoJSON will also be converted to Well known Text (OPTIMISED_WKT_<zoomlevel>; )using the functionality in the GeoJSONtoWKT service. This allows SQL Server to support geoJSON;
Simplified GeoJSON is always stored in SRID 4326 (WGS 84 as used by GPS);
Simplify tolerance is the size of a pixel in 4326 units (degrees) and can be pre-calculated. All simplification carried out on the geoJSON so the units are always degrees;
Returns the bounding box on the shapefile and an array of area id and area name.

## Slide 14: Zoomlevels and simplify tolerance
Level | Degree | m/pixel | Approximate Scale | Simplify tolerance (degrees)
0 | 360 | 156412 | 1:500 Million | 1.40
1 | 180 | 78206 | 1:250 Million | 0.70
2 | 90 | 39103 | 1:150 Million | 0.35
3 | 45 | 19551 | 1:70 Million | 0.18
4 | 22.5 | 9776 | 1:35 Million | 0.09
5 | 11.25 | 4888 | 1:15 Million | 0.04
6 | 5.625 | 2444 | 1:10 Million | 0.022
7 | 2.813 | 1222 | 1:4 Million | 0.011
8 | 1.406 | 610.9 | 1:2 Million | 0.0055
9 | 0.703 | 305.4 | 1:1 Million | 0.0027
10 | 0.352 | 152.7 | 1:500000 | 0.0014
11 | 0.176 | 76.37 | 1:250000 | 0.00069

## Slide 15: GeoJSON conversions
Convert GeoJSON to:
TopoJSON using the toTopoJSON service;
Well known text using the GeoJSONtoWKT service;
Usually not run directly as called from the simplifyGeoJSON service;
You will get the converted data back;

## Slide 16: Create hierarchy tables
The createHierarchy service:
Using the control table a GeoSpatial intersection of all the shapefiles is calculated in a further table with metadata stored in the control table as geolevel id (1 to max shapefiles in set) for each shapefile and related file;
The algorithm differs from the ArcGIS in that where intersections overlap (e.g. level4 appears in more than 1 lower resolution level3) the level3 with the greatest intersected area is chosen;
You get the hierarchical data back.

## Slide 17: Control Table
Contains session id, table name and file name;
One row per shapefile or processed table;
Parent table if a processed table;
XML metadata if present in shapefile set;
Geolevel id after hierarchy intersection (createHierarchy service);
Area id and area name field metadata after the simplifyGeoJSON service has been run;

## Slide 18: Create maptiles
The createMapfiles service:
Creates topoJSON maptiles for all geolevels and zoomlevels - 0 to the highest resolution zoomlevel (11 by default) within the area bounds of the shapefile;
This is placed into a further table with metadata stored into the control;
For efficiency only maptiles within the bounds of the shapefile are created;
You will get a summary of maptile data back. A separate per maptile get method is provided,

## Slide 19: Centroids
The createCentroids service will create polygonal and population weighted centroids:
Polygonal uses ST_Centroid();
Population weighted centroids require an input population and a PostGIS method from the GIS team;

## Slide 20: Potential issues
Slivers in input shapefiles. These can potentially be removed using quantization;
Timeouts. Simplification and maptile generation are long operations. A move to a batch processing model may be required.

## Slide 21: Services

## Slide 22: List of services
Shp2GeoJSON: Upload then convert shapefile to geoJSON;
simplifyGeoJSON: Load, validate, aggregate, clean and simplify converted shapefile data;
toTopoJSON: Convert geoJSON to TopoJSON;
GeoJSONtoWKT: Convert geoJSON to Well Known Text (WKT);
createHierarchy: Create hierarchical geospatial intersection of all the shapefiles;
createCentroids: Create centroids for all shapefiles;
createMaptiles: Create topoJSON maptiles for all geolevels and zoomlevels;
getGeospatialData: Fetches GeoSpatial Data;
getNumShapefilesInSet: Returns the number of shapefiles in the set. This is the same as the highest resolution geolevel id;
getMapTile: Get maptile for specified geolevel, zoomlevel, X and Y tile number.

## Slide 23: Shp2GeoJSON service
Upload then convert shapefile to geoJSON;
Input fields:
Name: shapefileBaseName Format: ESRI shapefile name without the extension;
Name: geometryColumn Format: Valid database column name;
Name: sessionId Format: HEX string; NULL for first shapefile in session;
Name: store Format: Text (true/false). If true [default] stored in server.
Mandatory input files (required; may be Gzip or lz77 compressed):
.shp – ESRI shapefile;
.dbf – Dbase IV database files;
.prj – ESRI projection file;
.smp.xml – Shapefile geospatial metadata (ISO 19115) [OPTIONAL];
All other extension types (.sbn, .sbx, .fbn, .fbx, .ain, .aih, .ixs, .mxs, .atx, .cpg, .qix) are saved but otherwise ignored.

## Slide 24: Shp2GeoJSON service (2)
Output JSON:
Name: wkt Format: Well Known Text; returned if store=false;
Name: sessionId Format: HEX string; autogenerated if sessionId is null;
Name: geoJson Format: GeoJSON; returned if store=false.

## Slide 25: simplifyGeoJSON
Load, validate, aggregate, clean and simplify converted shapefile data;
Input fields:
Name: GeoJson Format: GeoJSON;
Name: shapefileBaseName Format: ESRI shapefile name without the extension;
Name: sessionId Format: HEX string;
Name: areaIdColumn Format: Valid database column name;
Name: areaNameColumn Format: Valid database column name;
Name: simplify Format: dp/visvalingam/weighted (See: https://github.com/mbloch/mapshaper/wiki/Command-Reference)
Name: Zoomolevels Format: An array of integer zoomlevels (0-19); default [6,8,11]

## Slide 26: simplifyGeoJSON service (2)
Output JSON:
Name: boundingBox Format: Object [
double precision xmin, double precision ymin,
double precision xmax, double precision ymax,
integer srid];
Name: lookupTable Format: An array of area id and area name pairs.

## Slide 27: toTopoJSON service
Convert geoJSON to TopoJSON;
Input fields:
Name: Geojson Format: geoJSON
Output JSON:
Name: topojson Format: topoJSON

## Slide 28: GeoJSONtoWKT service
Convert geoJSON to Well Known Text (WKT);
Input fields:
Name: Geojson Format: geoJSON;
Output JSON:
Name: wkt Format: Well Known Text

## Slide 29: createHierarchy service
Create hierarchical geospatial intersection of all the shapefiles;
Input fields:
Name: sessionId Format: HEX string;
Output JSON:
Name: hierarchyTable Format: Table of text; column names:
  areaIdColumn of lowest resolution shapefile … areaIdColumn of highest resolution shapefile, e.g. coa2011, soa2011, ward2011, ladua2011, gor2011.

## Slide 30: createCentroids service
Create centroids for all shapefiles;
Input fields:
Name: sessionId Format: HEX string;
Name: hasHeader Format: true/false (as text)
Name: Header Format: JSON array, default [areaId,males,females]; names must be as per default.
Optional input file:
.csv: Male and female population by area_id. No header: assume area ID, total males, total females
Output JSON:
Name: centroidTable Format: Table with column names:
  areaId: Area ID;
  Xcoordinate: Polygonal X co ordinate;
  YCoordinate : Polygonal y co ordinate;
  XPopCoordinate: Population weighted X co ordinate;
  YPopCoordinate : Population weighted y co ordinate

## Slide 31: createMaptiles service
Create topoJSON maptiles for all geolevels and zoomlevels;
Input fields:
Name: sessionId Format: HEX string;
Output JSON:
Name: mapTileTable Format: Table with column names:
  shapefileBaseName: Name of geolevel;
  Zoomlevel: Zoomlevel (0-max zoomlevel, default: 11, maximum: 19);
  geolevelId: Numeric geoLevel after hierarchy created (1-number of shapefiles);
  numTiles: Number of tiles in zoomlevel and geolevel;
  minX: Minimum X tile number;
  maxX: Maximum X tile number;
  minY: Minimum Y tile number;
  maxY: Maximum Y tile number;

## Slide 32: getGeospatialData service
Fetches GeoSpatial Data. Normally called after all other processing is completed, one data set per original shapefile;
Input fields:
Name: sessionId Format: HEX string;
Name: shapefileBaseName Format: Valid database column name, name of geolevel and also of original shapefile;

## Slide 33: getGeospatialData service (2)
Output JSON:
  Cleaned and valid original data as geoJSON (ShapefileGeoJSon) and Well Known Text (ShapefileWkt);
  OptimisedGeojsonZoomlevel<zoomlevel>, OptimisedWktZoomlevel<zoomlevel>: Simplified data as geoJSON and Well Known Text (WKT);
  GeolevelId: Geolevel ID (1 to max shapefiles in set) if hierarchical intersection created;
  ShapefileMetadata: Shapefile XML metadata in JSON format if present;
  Projection: Original projection;
  Srid: SRID
  AreaId, AreaName: area id and area name field data;
  Polygonal and population weighted centroids (see: createCentroids)

## Slide 34: getNumShapefilesInSet service
Returns the number of shapefiles in the set. This is the same as the highest resolution geolevel id;
Input fields:
Name: sessionId Format: HEX string;
Output JSON:
Name: numShapefiles Format: Integer.

## Slide 35: getMapTile service
Get maptile for specified geolevel, zoomlevel, X and Y tile number. The createMaptiles service return the table data needed to iterate through all the tiles;
Input fields:
Name: sessionId Format: HEX string
Name: Zoomlevel Format Integer, zoomlevel (0-max zoomlevel, default: 11, maximum: 19);
Name: geolevelId Format: Integer, numeric geoLevel after hierarchy created (1-number of shapefiles);
Name: XTileId Format: Integer;
Name: YTileId Format: Integer;
Output JSON:
Name: mapTile Format: topoJSON.